## Slide 1: NRCS PRACTICES TO REDUCE SOIL EROSION

## Slide 2: PATHWAYS TO REDUCE SOIL EROSION
Field scale management changes
  Increase water storage in the soil
  Examples
    Cover crops
    No-Till
Notes: 20,000 ga/acre = additional storage for ¾” rainfall

## Slide 3: PATHWAYS TO REDUCE SOIL EROSION
Establish stable areas for water to move through
  Construct stabilized waterways
    Grassed waterway
  Improve stream bank stability
    Vegetated buffers
    Riparian tree planting
    Streambank stabilization projects- $$
Grassed Waterway
Stabilized Stream Coridor

## Slide 4: PATHWAYS TO REDUCE SOIL EROSION
Create water holding structures
  Short term structures hold water back and release it over a longer duration (24-48 hours)
  Slowing water velocity reduces the sediment it can carry
    Urban-
      water detention basin
    Agricultural
      Water & Sediment control basin
      Terraces
Terrace
Terrace
Water Level during rainfall
Trapped sediment
Water Inlet

## Slide 5: PATHWAYS TO REDUCE SOIL EROSION
Construct Grade Stabilization Structures
  Water impounding grade stabilization structures back water over the unstable grade
    Farm Ponds
  Structures can be built to armor the area of erosion
    Rock Chutes
    Fabric lined chutes
Headcut formed from water
moving over an unstable grade
Farm Pond
Rock Chute

## Slide 6: PROCESS FOR SELECTING EROSION CONTROL PRACTICES
Determine the underlying cause of the erosion
  Why has the erosion taken place?
  What type of erosion is occurring
Understand the Landowner’s goals and management system
  Equipment sizes
  Management preferences

## Slide 7: PROCESS FOR DESIGNING EROSION CONTROL PRACTICES
Landscape factors in structure design
  Watershed length and slope
  Soil type
  Land use/ management
    Sediment loss
Environmental factors in structure design
  Rainfall amount
  Rainfall duration
  Most designs are based on a 4.5 inch rainfall event over 24 hours

## Slide 8: Questions